Atari Budget Cartridge Programmer
Serial Protocol

Author:	Justin Lane (atari2600@jigglesoft.co.uk)
Date:	2019-02-21 21:44
Version:	0.0.2

# Introduction
This document details the serial protocol used for communication between the programming application tool and the budget cartridge programmer firmware. The budget cartridge programmer has a USB CDC interface that is used to connect the PC. The budget cartridge programmer is powered from the USB interface. The cartridge budget programmer has two cartridge ports. Firstly there is a flash memory cartridge port that can be used to program the budget flash memory cartridge or the flash memory, RAM, and PLD cartridge. Secondly there is also an Atari 7800 cartridge port that can be used to dump Atari 2600 or Atari 7800 ROM images.

Personal
Computer

Budget
Cartridge
Programmer
Cartridge
ROM/
Flash

Programming
Application
Tool

USB CDC Cartridge Programmer Serial Protocol

# USB CDC Serial Communication Protocol

## Protocol Overview
Serial communication is 8 data bits, no parity, and one stop bit.
Only the ASCII (lower 7 bits) of the each data byte is used.
The protocol being simple ASCII text allows terminal or expects scripts to drive programming and is useful for testing.
The protocol is driven from the PC as a request / response(s).
The protocol is made up lines.
There is a limit of 160 bytes per line.
The line is terminated with a LF.
CR is ignored.
If the line length is exceeded the line is marked as invalid and all bytes up to and including the LF are discarded. Upon receipt of the LF a line overflow error state is returned.
The line is prefixed with a line class indicator character, the command name, then optionally a comma and any arguments.
Upon receipt of a LF the programmer will parse, process, and issue a response.
The response will consist of an error code and any data.
The request is limited to one line per request.
The response is is not limited to one line per request.

Examples

Request and single response

Request:
?CART_DETECT
Response:
=0|1|#Flash

Request and single error response

Request:
?CART_CONNECT
Response:
=2|Cartridge already connected!

Request and multiple responses

Request:
!PC<PROG|SECTOR|E0
Response:
? error code – multi part – what part ???
<SECTOR|E0|0000|000F|00 01 02 03 04 05 06 07 08 09 0A 0B 0C 0D 0E 0F
<

Request and error during multiple responses (1)

Request and error during multiple responses (2)

Request and error during multiple responses (3)

## Protocol Command Summary
### Common
Command	Code	Input	Output	Notes
Reset Programmer	!RESET	[WARM|COLD]
Query Cartridge Detection	?CART_DET	N/A	0=None,1=Flash, 2=ROM, 3=Flash+ROM!
Query Version Info	?VERSION	N/A	Application Version,Application Protocol Version,PC Driver Version,Firmware Version,Firmware Protocol Version, Hardware Version
Connect to Cartridge	!CONNECT	1=Flash, 2=ROM
Disconnect from Cartridge	!DISCONNECT
Query Programmer Capabilities
Query Cartridge Capabilities
Query Low-Level Capabilities
Detect Cartridge Type
Set Options, Get Options

### Low-Level Access

### Programmable Flash ROM

### Legacy ROM Cartridge Dumper

Group	Command	Code	Request	Response
Common

Low-Level

	Reset Programmer	!RESET

Legacy ROM Cartridge Dumper

Terminology
Sector:	4KB bank/page of ROM

Lines terminated by LF (CR ignored).
Anything following ‘;’ is ignored (comments).
Buffer is filled with chars. On LF and buffer not overflow parse and execute.
On Comment ‘;’ stop filling buffer.
Max line length = 128
Lines start with:
; = Comment
< = Download
> = Upload
{ = Rip Cart Data
} = Write Cart Data
? = Query
! = Command

= = Result
~ = Abort???
# = ???
* = ???
## Protocol Command Details
## Common
### Hello
Send LF’s UNTIL
; HELLO

????

### Reset
### Request Status
?STATUS
### Request Cartridge Detection
Detect Cartridge:
Input (command):	DET_CART
Output (bitmap):	0 = None, 1 = ROM, 2 = Flash, 3 = ROM+Flash (error)

query programmer capabilities
query programmer versions
connect/open to cartridge
disconnect/close cartridge

Checksums

## Low Level Access
Get Info Pin, Type, Min,Max, … TODO
Set Pin Value
Get Pin Value
Set Pin DDR
Get Pin DDR
Get Port Value
Set Port Value
Get Port DDR
Set Port DDR

## Programmable Flash ROM
This is the mechanism for programming the budget flash memory cartridges.
### Request Flash Memory Info
Request:	?FLASH_INFO
Return (data):	#Manufacturer=Manufacturer
Return (data):	#Size in Bytes=Size In Bytes
Return (data):	#Sector Size in Bytes=Sector Size in Bytes
Return (success):	=0,Success Message
Return (failure):	=Error Code,Error Description

### Erase All Flash Memory
Request:	!FLASH_ERASE_ALL
Return (success):	=0,Success Message
Return (failure):	=Error Code,Error Description

### Erase Flash Memory Sector
Request:	!FLASH_ERASE_SECTOR,Sector Number
Return (success):	=0,Success Message
Return (failure):	=Error Code,Error Description

!FLASH_ERASE,SECTOR,Sector Number

Return (progress):	@Percentage

### Download from Programmer RAM to PC
<RAM
<RAM,Start Address,End Address

### Upload from PC to Programmer RAM
>RAM,Start Address,End Address,
#Data

### Download to Programmer RAM from Flash ROM
<ROM,
### Upload from Programmer RAM to Flash ROM

### YYY Info

## ROM Dumper

### XXX Size

### YYY Info