Atari 2600
2K/4K Budget ROM Cartridge and Programmer

Author:	Justin Lane (atari2600@jigglesoft.co.uk)
Date:	2019-01-23 21:28
Version:	0.0.0

# Introduction
This document describes an extremely low cost Atari 2600 cartridge PCB and associated programmer for home-brew development of 2K/4K ROM software.

# Requirements
## Cartridge
- Extremely low cost. Aim is < $3 cost per populated cartridge.
- Support 2K or 4K ROM images.
- Modern components.
- Supports use without an enclosure.
- Fits into standard cartridge enclosure or simple enclosure.
- Open Source design.
- Optionally support multiple 4K ROM banks by manual selection (DIP switches).
## Programmer
- Extremely low cost. Aim is < $10 per programmer hardware.
- Support 2K or 4K ROM images.
- Modern components.
- Allows programming of the 2K/4K cartridge above.
- Allows programming all banks for whole chip 128KB, 256KB, or 512KB.
- Open Source hardware design.
- Closed source firmware, driver, and software tooling. This is to be reviewed.

# Existing Cartridges
http://www.retrogamenetwork.com/wp-content/uploads/2018/05/atariboards.png

https://i.ebayimg.com/images/g/ch0AAOSw19dcLFyD/s-l1600.jpg

https://i.ebayimg.com/images/g/qmMAAOSwmXpcLFyC/s-l1600.jpg

# Candidate Components

SST39SF010A-55-4I-NHE	1Mbit = 256KB	PLCC

SST39SF010A	4Mbit = 512KB

A0-A7 + A8-A11
A12 = -ROM Select

A0-A11 = 4K

A12 8K
A13 16K
A14 32K
A15 64KB

A16 128KB
A17 256KB
A18 512KB

# Implementation

IS62C1024AL
IS65C1024AL

https://www.mouser.co.uk/datasheet/2/198/62-65C1024AL-258436.pdf

## Schematic

## BOM

## PCB

# Estimated Costs

# Programmer

ATMEGA4809

Part Number: DM320115 - ATmega4809 Curiosity Nano Evaluation kit

# References

- Optionally support single 128KB, 256KB, or 512KB ROM via 3F bank switching.
ATF1502ASL-25JU44
CPLD from Microchip (Atmel)

Frame = 6 bytes (5.5 = 40bits PF) * 25 = 250 bytes / frame
11 frames / second = 2750 Bytes / second
256MB / 2750 Bytes = 97,612seconds = 1626 minutes.
<<<WRONG – CHIP IS KB NOT MB>>>
Could convert movie to Atari 2600 using mode 3F.
Great idea for technical demonstration.

Would support samples too.
50 x 300 = 15000 Hz 15KHz – movies could have full sound !!!!!

Great to have an Atari Game with cut scenes.

Also could have DPC+??? or at least DPC
Maybe sprite enhancements – sprite tracking. Maybe an FPGA for that one in the future.

Programmer Pinouts

Nano / Pin	Name	Flash. / Pin	Name	2600 / Pin	Name	7800 / Pin	Name	5200 / Pin	Name
		24	A0	20	A0	29	A0	19
		23	A1	19	A1	28	A1	20
		22	A2	18	A2	27	A2	17
		21	A3	17	A3	26	A3	21
		20	A4	16	A4	25	A4	22
		19	A5	15	A5	24	A5	16
		18	A6	14	A6	23	A6	15
		17	A7	13	A7	22	A7	27
		7	A8	10	A8	13	A8	29
		6	A9	9	A9	12	A9	31
		3	A10	7	A10	10	A10	33
		5	A11 (4KB)	8	A11 (4KB)	11	A11	35
		16	A12 (SW)	6	A12 (CS)	9	A12	34
		8	A13 (SW)		-			32	A13
		9	A14 (SW)		-
		15	A15 (SW)		-
		14	A16 (128K)		-
		10	A17 (256K)		-
		13	A18 (512K)		-
		25	D0	21	D0	30	D0	1
		26	D1	22	D1	31	D1	2
		27	D2	23	D2	32	D2	3
		29	D3	1	D3	4	D3	4
		30	D4	2	D4	5	D4	5
		31	D5	3	D5	6	D5	6
		32	D6	4	D6	7	D6	7
		1	D7	5	D7	8	D7	8
		2	-CE		-
		4	-OE		-
		11	-WE		-
		12	VDD	11	+5V	14		26
		28	VSS	24	GND	33		12, 13, 23, 25	GND
				12	-EXROM	15
						1	R/-W
						2	HALT
						3	<INTERLOCK>
						16	<INTERLOCK>
						17	A13
						18	A14
						19	A15
						20	EAUDIO	30	Audio In (2 port)???
						21	<INTERLOCK>
						34	<INTERLOCK>
						35	IRQ
						36	02CLK
								9	Enable 80-8F
								10	Enable 40-7F
								11	<No-Connect>
								18, 36	<INTERLOCK>
								28	<No-Connect>
								24??????
								14?????