Atari Budget Cartridge Programmer
Serial Protocol

Author:	Justin Lane (atari2600@jigglesoft.co.uk)
Date:	2019-02-21 21:44
Version:	0.0.2

# Introduction
This document details the serial protocol used by the programming application tool to communicate with the budget cartridge programmer firmware. The budget cartridge programmer has a USB CDC interface that is used to connect the PC. The budget cartridge programmer is powered from the USB interface. The cartridge budget programmer has two cartridge ports. There is a flash memory cartridge port that can be used to program the budget flash memory cartridge or the budget flash memory, RAM, and PLD cartridge. There is also an Atari 7800 cartridge port that can be used to dump Atari 2600 or Atari 7800 ROM’s.

Personal
Computer

Budget
Cartridge
Programmer
Cartridge
ROM/
Flash

Programming
Application
Tool

USB CDC Cartridge Programmer Serial Protocol

# USB CDC Serial Communication Protocol

## Protocol Overview

## Protocol Command Summary
### Common
Command	Code	Input	Output	Notes
Reset Programmer	!RESET	[WARM|COLD]
Query Cartridge Detection	?CART_DET	N/A	0=None,1=Flash, 2=ROM, 3=Flash+ROM!
Query Version Info	?VERSION	N/A	Application Version,Application Protocol Version,PC Driver Version,Firmware Version,Firmware Protocol Version, Hardware Version
Connect to Cartridge	!CONNECT	1=Flash, 2=ROM
Disconnect from Cartridge	!DISCONNECT
Query Programmer Capabilities
Query Cartridge Capabilities
Query Low-Level Capabilities
Detect Cartridge Type
Set Options, Get Options

### Low-Level Access

### Programmable Flash ROM

### Legacy ROM Cartridge Dumper

Group	Command	Code	Request	Response
Common

Low-Level

	Reset Programmer	!RESET

Legacy ROM Cartridge Dumper

Terminology
Sector:	4KB bank/page of ROM

Lines terminated by LF (CR ignored).
Anything following ‘;’ is ignored (comments).
Buffer is filled with chars. On LF and buffer not overflow parse and execute.
On Comment ‘;’ stop filling buffer.
Max line length = 128
Lines start with:
; = Comment
< = Download
> = Upload
{ = Rip Cart Data
} = Write Cart Data
? = Query
! = Command

= = Result
~ = Abort???
# = ???
* = ???
## Protocol Command Details
## Common
### Hello
Send LF’s UNTIL
; HELLO

????

### Reset
### Request Status
?STATUS
### Request Cartridge Detection
Detect Cartridge:
Input (command):	DET_CART
Output (bitmap):	0 = None, 1 = ROM, 2 = Flash, 3 = ROM+Flash (error)

query programmer capabilities
query programmer versions
connect/open to cartridge
disconnect/close cartridge

Checksums

## Low Level Access
Get Info Pin, Type, Min,Max, … TODO
Set Pin Value
Get Pin Value
Set Pin DDR
Get Pin DDR
Get Port Value
Set Port Value
Get Port DDR
Set Port DDR

## Programmable Flash ROM
This is the mechanism for programming the budget flash memory cartridges.
### Request Flash Memory Info
Request:	?FLASH_INFO
Return (data):	#Manufacturer=Manufacturer
Return (data):	#Size in Bytes=Size In Bytes
Return (data):	#Sector Size in Bytes=Sector Size in Bytes
Return (success):	=0,Success Message
Return (failure):	=Error Code,Error Description

### Erase All Flash Memory
Request:	!FLASH_ERASE_ALL
Return (success):	=0,Success Message
Return (failure):	=Error Code,Error Description

### Erase Flash Memory Sector
Request:	!FLASH_ERASE_SECTOR,Sector Number
Return (success):	=0,Success Message
Return (failure):	=Error Code,Error Description

!FLASH_ERASE,SECTOR,Sector Number

Return (progress):	@Percentage

### Download from Programmer RAM to PC
<RAM
<RAM,Start Address,End Address

### Upload from PC to Programmer RAM
>RAM,Start Address,End Address,
#Data

### Download to Programmer RAM from Flash ROM
<ROM,
### Upload from Programmer RAM to Flash ROM

### YYY Info

## ROM Dumper

### XXX Size

### YYY Info